## Slide 1: ACURATE neo2TM v SAPIEN 3 UltraTM Head-to-Head Comparison

## Slide 2
Device Overview ACURATE neo2 & SAPIEN 3 Ultra
CAUTION: In Europe, ACURATE neo and neo2 Aortic Valve Systems are CE-marked. In the USA, ACURATE neo2 is an investigational device and restricted under federal law to investigational use only. Not available for sale.
ACURATE neo2 Aortic Valve System
Porcine Pericardium, Supra Annular Leaflets
Self-Expanding (Top-down) Nitinol frame
CE marked 2020
Not FDA Approved, Investigational Device in the US
SAPIEN 3 Ultra Transcatheter Heart Valve
Bovine Pericardium, Intra-annular Leaflets
Balloon-Expanding Cobalt-Chromium Frame
CE marked 2018
FDA Approved 2018
Notes: [DELIVERY NOTES]
ACURATE neo2 maintains key features of the ACURATE Platform:
  14F iSLEEVE Introducer compatible
  Self-expanding nitinol frame with porcine pericardium leaflets
  Supra-annular positioning; two-step top-down deployment
  Treats annuli from 21 mm to 27 mm
  Sizes S –23 mm, M –25 mm, L –27 mm
Includes the ACURATE neo2 Active PVsealTM Technology to minimize moderate/severe PVL and overall burden of paravalvular leak and Radiopaque Positioning Marker for placement accuracy

## Slide 3
Study Design 1st head-to-head comparison of ACURATE neo2 & SAPIEN 3 Ultra
CAUTION: In Europe, ACURATE neo and neo2 Aortic Valve Systems are CE-marked. In the USA, ACURATE neo2 is an investigational device and restricted under federal law to investigational use only. Not available for sale.
Head-to-Head Transfemoral TAVR
n = 1356 Patients | 4 German Centers | Procedures performed: March 2019 – December 2021
Objective: To compare VARC-3 device and technical success (Primary Endpoint)
and 30-day VARC-3 clinical endpoints (Secondary Endpoint) of
ACURATE neo2 to SAPIEN 3 Ultra
1:1 nearest neighbour matching |  | 
Age Female gender EuroScore I NYHA III/IV Coronary artery disease | Previous PCI Mean transvalvular gradient LVEF < 35% Bicuspid aortic valve | Mean annulus diameter Severe calcification Asymmetric calcification Indexed Effective Orifice Area (iEOA)
ACURATE neo2
n=608
SAPIEN 3 Ultra
n=748
ACURATE neo2
n=472
SAPIEN 3 Ultra
n=472
Pellegrini C. ACURATE neo2 versus SAPIEN 3 Ultra. EuroIntervention 2022.
Notes: [DELIVERY NOTES]
Outcomes from a German multicenter comparison of the ACURATE neo2 and SAPIEN 3 Ultra TAVR valves were presented by Dr Won-Keun Kim from the Kerckhoff Klinik (Bad Nauheim, Germany) at the EuroPCR Congress 2022.
First direct head-to-head comparison of the 2nd generation ACURATE neo2 and 4th generation SAPIEN 3 Ultra valves
This study enrolled all eligible patients for both devices from respective commercial availability. SAPIEN 3 Ultra was CE marked November 2018 and ACURATE neo2 was CE marked April 2020 & commercialized September 2020. The inclusion of all patients treated in this extended time period allows for improved validity of the analysis.

## Slide 4
Baseline Characteristics
ACURATE neo2 & SAPIEN 3 Ultra
 | Matched population |  | 
 | ACURATE neo2 n=472 | SAPIEN 3 Ultra n=472 | p-value
Age, years | 82.0 [78.7 – 85.0] | 81.6 [77.6 – 85.1] | 0.584
Female gender | 239 (50.6) | 246 (52.1) | 0.696
Logistic EuroScore, % | 13.8 [7.9 – 23.0] | 12.5 [7.9 - 21.9] | 0.184
NYHA III/IV | 305 (64.6) | 297 (62.9) | 0.636
Coronary artery disease | 340 (72.0) | 336 (71.2) | 0.829
Previous myocardial infarction | 50 (10.6) | 54 (11.4) | 0.755
Previous stroke | 57 (12.1) | 55 (11.7) | 0.920
COPD | 57 (12.1) | 56 (11.9) | 0.999
Peripheral artery disease | 61 (12.9) | 81 (17.2) | 0.083
eGFR, ml/min | 65.0 [47.0 – 84.3] | 62.0 [47.7 – 79.0] | 0.198
Previous pacemaker | 57 (12.1) | 46 (9.7) | 0.296
Atrial fibrillation | 190 (40.3) | 191 (40.5) | 0.999
Right bundle-branch block | 50 (10.6) | 60 (12.7) | 0.361
LVEF <35% | 17 (3.6) | 13 (2.8) | 0.579
Mean gradient, mmHg | 43.0 [34.0 – 52.0] | 42.5 [34.8 – 51.0] | 0.940
Bicuspid aortic valve | 20 (4.2) | 25 (5.3) | 0.542
Severe aortic valve calcification | 114 (24.3) | 115 (24.4) | 0.954
Asymmetric calcification | 120 (25.4) | 135 (28.6) | 0.305
Mean annulus diameter, mm | 23.8 [22.4, 25.2] | 24.9 [23.4, 26.2] | <0.001
CAUTION: In Europe, ACURATE neo and neo2 Aortic Valve Systems are CE-marked. In the USA, ACURATE neo2 is an investigational device and restricted under federal law to investigational use only. Not available for sale.
Pellegrini C. ACURATE neo2 versus SAPIEN 3 Ultra. EuroIntervention 2022.
NOTE: 1:1 Propensity Score-Matching (PSM) was performed to reduce any imbalance in baseline demographics, and clinical & echocardiographic characteristics from the entire population
Notes: Delivery Notes:
After 1:1 matching, the only significant difference seen in baseline characteristics is mean annulus diameter.

## Slide 5
Essential Outcomes
ACURATE neo2 & SAPIEN 3 Ultra
CAUTION: In Europe, ACURATE neo and neo2 Aortic Valve Systems are CE-marked. In the USA, ACURATE neo2 is an investigational device and restricted under federal law to investigational use only. Not available for sale.
 | ACURATE neo2 n=472 | SAPIEN 3 Ultra n=472 | p-value
Pre-dilatation, n (%) | 434 (91.9) | 148 (31.4) | <0.001
Post-dilatation, n (%) | 211 (44.7) | 69 (14.6) | <0.001
Procedural time, min | 45.0 [36.0 – 59.0] | 46.0 [35.0 – 57.0] | 0.472
Fluoroscopy time, min | 9.8 [7.3 - 13.8] | 10.2 [6.9 - 14.1] | 0.974
Technical success (VARC-3) ‡ | 448 (94.9) | 450 (95.3) | 0.880
Device success (VARC-3)‡‡ | 434 (91.9) | 401 (85.0) | 0.001
Contrast agent, ml | 40.0 [22.0, 130.0] | 117.5 [37.8, 160.0] | <0.001
Pre-discharge moderate/severe PVL n (%)* | 3 (0.6) | 5 (1.1) | 0.723
Pre-discharge Mean gradient ≥ 20mmHg, n (%) | 11 (2.4) | 36 (7.7) | <0.001
Indexed effective orifine area (cm2)** | 0.9 [0.8, 1.1] (n=342) | 0.8 [0.7, 0.9] (n=167) | <0.001
Severe PPM, n (%)** | 10/342 (2.9) | 25/167 (15.0) | <0.001
Major vascular complication (VARC-3) | 29 (6.1) | 45 (9.5) | 0.069
Coronary obstruction requiring PCI | 1 (0.2) | 2 (0.4) | 0.999
Annular rupture, n (%) | 1 (0.2) | 0 (0) | 0.999
Acute Kidney Injury Network (AKIN) 2-4, n (%) | 15 (3.2) | 15 (3.2) | 0.999
30-day All-stroke** | 16/464 (3.4) | 11/465 (2.4) | 0.435
30-day Pacemaker implantation, n (%)** | 33/406 (8.1) | 43/419 (10.3) | 0.289
30-day mortality, n (%)** | 8/464 (1.7) | 11/465 (2.4) | 0.646
*Pre-discharge echocardiogram assessed. 10/1356 assessed by angio
** Data not available for full population. Sample sizes as indicated.
Pellegrini C. ACURATE neo2 versus SAPIEN 3 Ultra. EuroIntervention 2022.
NOTE: Reported outcomes reflect the PSM population. Outcomes for the entire population are in line with PSM results.
‡ Defined as Freedom from mortality. Successful access, delivery of the device and retrieval of the delivery system. Correct positioning of a single prosthetic heart valve into the proper anatomical location. Freedom from surgery or intervention related to the device or to a major vascular or access-related, or cardiac structural complication.
‡‡Defined as freedom from mortality, surgery or intervention related to the device or to a major vascular or access-related or cardiac structural complication and intended performance of the valve (mean gradient <20 mmHg, peak velocity <3 m/s, Doppler velocity index =0.25 and less than moderate AR).
Notes: Delivery Notes:
This is the 1st direct head-to-head comparative study of the 2nd generation ACURATE neo2 and 4th generation SAPIEN 3 Ultra valves, demonstrating favorable ACURATE neo2 outcomes:
  Paravalvular Leak: The rate of echocardiogram assessed moderate to severe PVL was low and similar for both THVs (0.6% vs. 1.1%, p=0.723). ACURATE neo2 recorded 32.8% mild and 66.5% none PVL rates1.
  Gradients: ACURATE neo2 demonstrated significantly lower mean gradients (9±4 vs 13±4 mmHg; p<0.001), and a lower rate of elevated (≥20mmHg) gradients (2.4% vs 7.7%; p<0.001) and significantly larger Indexed Effective Orifice Area (iEOAs) (0.92cm2 [0.79, 1.05] vs. 0.78 cm2 [0.67, 0.91]; p<0.001)‡. This translated into a significantly lower rate of severe prosthesis-patient mismatch (2.9% vs 15.0%; p<0.001‡) and a superior device success rate (91.9% vs. 85%; p=0.001) for ACURATE neo21
  Permanent Pacemaker Implantation: The 30-day new permanent pacemaker implantation rate was low and similar for both THVs (8.1% vs 10.3%; p=0.289)*1.
  In-Hospital & 30-day Events: Rates of in-hospital and 30-day events were overall low, and comparable between both THVs1.

## Slide 6
Chart: 
| Category 1
None or trace | 0.789
Mild | 0.2
Moderate or severe | 0.011
Moderate or Severe
Mild
None
Chart: 
| Category 1
None or trace | 0.665
Mild | 0.328
Moderate or severe | 0.006
0.6%
ACURATE
neo2
SAPIEN 3
Ultra
P = 0.686
1.1%
Essential Matched Cohort Outcomes
ACURATE neo2 & SAPIEN 3 Ultra
CAUTION: In Europe, ACURATE neo and neo2 Aortic Valve Systems are CE-marked. In the USA, ACURATE neo2 is an investigational device and restricted under federal law to investigational use only. Not available for sale.
Similar and low Rates of PVL
Lower Mean Gradients
Lower Severe Prothesis-Patient Mismatch
0.6% Moderate to Severe PVL vs. 1.1% with SAPIEN 3 Ultra p=0.723 | 2.4% Elevated Gradients* vs. 7.7% with SAPIEN 3 Ultra p < 0.001 | 91.9% Device success vs. 85.0% with SAPIEN 3 Ultra p = 0.001
*(≥ 20mmHg)
Pellegrini C. ACURATE neo2 versus SAPIEN 3 Ultra. EuroIntervention 2022.
ACURATE neo2
2.9% Severe PPM
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 0.023 | 0.977
2.9%
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 0.155 | 0.977
15.0%
SAPIEN 3 Ultra
15.0% Severe PPM
P < 0.001
Before TAVR
After TAVR
ACURATE
neo2
SAPIEN 3
Ultra
43+9 vs 43+8 mmHg
P = 0.940
9+4 vs 13+4 mmHg
P < 0.001
Notes: Delivery Notes:
This is the 1st direct head-to-head comparative study of the 2nd generation ACURATE neo2 and 4th generation SAPIEN 3 Ultra valves, demonstrating favorable ACURATE neo2 outcomes:
  Paravalvular Leak: The rate of echocardiogram assessed moderate to severe PVL was low and similar for both THVs (0.6% vs. 1.1%, p=0.723). ACURATE neo2 recorded 32.8% mild and 66.5% none PVL rates1.
  Gradients: ACURATE neo2 demonstrated significantly lower mean gradients (9±4 vs 13±4 mmHg; p<0.001), and a lower rate of elevated (≥20mmHg) gradients (2.4% vs 7.7%; p<0.001) and significantly larger Indexed Effective Orifice Area (iEOAs) (0.92cm2 [0.79, 1.05] vs. 0.78 cm2 [0.67, 0.91]; p<0.001)‡. This translated into a significantly lower rate of severe prosthesis-patient mismatch (2.9% vs 15.0%; p<0.001‡) and a superior device success rate (91.9% vs. 85%; p=0.001) for ACURATE neo21
  Permanent Pacemaker Implantation: The 30-day new permanent pacemaker implantation rate was low and similar for both THVs (8.1% vs 10.3%; p=0.289)*1.
  In-Hospital & 30-day Events: Rates of in-hospital and 30-day events were overall low, and comparable between both THVs1.

## Slide 7
Conclusions
ACURATE neo2 & SAPIEN 3 Ultra
1Pellegrini C. ACURATE neo2 versus SAPIEN 3 Ultra. EuroIntervention 2022. 2Herrmann HC, et al. J Am Coll Cardiol. December 4, 2018;72(22):2701-2711. 3Flameng, et al. Circulation. 2010;121:2123-2129. 4Pompeu Sá M, et al. Impact of Prosthesis-Patient Mismatch After Transcatheter Aortic Valve Replacement. JACC: Cardiovascular Imaging. 2022 Article In Press.
CAUTION: In Europe, ACURATE neo and neo2 Aortic Valve Systems are CE-marked. In the USA, ACURATE neo2 is an investigational device and restricted under federal law to investigational use only. Not available for sale.
First direct head-to-head propensity score matched comparison of the 2nd generation ACURATE neo2 and 4th generation SAPIEN 3 Ultra valves
Data from this study demonstrated:
  Low and similar rates of Moderate/Severe PVL (0.6% vs 1.1%; p=0.723)* and Permanent Pacemaker Implantation (8.1% vs 10.3%; p=0.289)** for ACURATE neo2 and SAPIEN 3 Ultra1
  Significantly lower rate of Elevated Gradients (2.4% vs. 7.7%; p<0.001)* for ACURATE neo2, resulting in a superior Device Success rate (91.9% vs. 85.0%; p=0.001)1
  ACURATE neo2 also demonstrated a lower rate of Severe Prosthesis-Patient Mismatch (2.9% vs 15.0%; p<0.001)*. Studies have demonstrated severe PPM to be associated with short and long-term mortality, heart failure rehospitalizations and premature structural valve degeneration1,2,3,4
* Pre-Discharge **30-day
Notes: Delivery Notes:
This is the 1st direct head-to-head comparative study of the 2nd generation ACURATE neo2 and 4th generation SAPIEN 3 Ultra valves, demonstrating favorable ACURATE neo2 outcomes:
  Paravalvular Leak: The rate of echocardiogram assessed moderate to severe PVL was low and similar for both THVs (0.6% vs. 1.1%, p=0.723). ACURATE neo2 recorded 32.8% mild and 66.5% none PVL rates1.
  Gradients: ACURATE neo2 demonstrated significantly lower mean gradients (9±4 vs 13±4 mmHg; p<0.001), and a lower rate of elevated (≥20mmHg) gradients (2.4% vs 7.7%; p<0.001) and significantly larger Indexed Effective Orifice Area (iEOAs) (0.92cm2 [0.79, 1.05] vs. 0.78 cm2 [0.67, 0.91]; p<0.001)‡. This translated into a significantly lower rate of severe prosthesis-patient mismatch (2.9% vs 15.0%; p<0.001‡) and a superior device success rate (91.9% vs. 85%; p=0.001) for ACURATE neo21
  Permanent Pacemaker Implantation: The 30-day new permanent pacemaker implantation rate was low and similar for both THVs (8.1% vs 10.3%; p=0.289)*1.
  In-Hospital & 30-day Events: Rates of in-hospital and 30-day events were overall low, and comparable between both THVs1.

## Slide 8
Study Limitations
ACURATE neo2 & SAPIEN 3 Ultra
CAUTION: In Europe, ACURATE neo and neo2 Aortic Valve Systems are CE-marked. In the USA, ACURATE neo2 is an investigational device and restricted under federal law to investigational use only. Not available for sale.
This is a non-randomized study, which incorporates 1:1 propensity matching (PSM), which does not fully exclude selection biases.
Site-reported data are reported. No independent Core-Laboratory or Clinical Event Committee adjudication have been used in this study.
Extremely calcified patients were excluded from this study.
Pellegrini C. ACURATE neo2 versus SAPIEN 3 Ultra. EuroIntervention 2022.

## Slide 9: Backup: Entire Population Baseline Characteristics and Essential Outcomes

## Slide 10
Baseline Characteristics
ACURATE neo2 & SAPIEN 3 Ultra
 | Entire population |  |  | Matched population |  | 
 | ACURATE neo2 n=608 | SAPIEN 3 Ultra n=748 | p-value | ACURATE neo2 n=472 | SAPIEN 3 Ultra n=472 | p-value
Age, years | 82.0 [78.7 – 85.0] | 81.4 [77.1 – 85.0] | 0.032 | 82.0 [78.7 – 85.0] | 81.6 [77.6 – 85.1] | 0.584
Female gender | 289 (47.5) | 398 (53.2) | 0.038 | 239 (50.6) | 246 (52.1) | 0.696
Logistic EuroScore, % | 14.4 [8.1 – 23.4] | 12.3 [7.7 - 21.3] | 0.008 | 13.8 [7.9 – 23.0] | 12.5 [7.9 - 21.9] | 0.184
NYHA III/IV | 420 (69.1) | 429 (57.4) | <0.001 | 305 (64.6) | 297 (62.9) | 0.636
Coronary artery disease | 376 (61.8) | 558 (74.6) | <0.001 | 340 (72.0) | 336 (71.2) | 0.829
Previous myocardial infarction | 58 (9.5) | 87 (11.6) | 0.251 | 50 (10.6) | 54 (11.4) | 0.755
Previous stroke | 77 (12.7) | 94 (12.6) | 0.999 | 57 (12.1) | 55 (11.7) | 0.920
COPD | 74 (12.2) | 86 (11.5) | 0.735 | 57 (12.1) | 56 (11.9) | 0.999
Peripheral artery disease | 84 (13.8) | 130 (17.4) | 0.085 | 61 (12.9) | 81 (17.2) | 0.083
eGFR, ml/min | 65.0 [47.0 – 83.0] | 64.0 [48.5 – 79.5] | 0.684 | 65.0 [47.0 – 84.3] | 62.0 [47.7 – 79.0] | 0.198
Previous pacemaker | 75 (12.3) | 71 (9.5) | 0.095 | 57 (12.1) | 46 (9.7) | 0.296
Atrial fibrillation | 256 (42.1) | 291 (38.9) | 0.243 | 190 (40.3) | 191 (40.5) | 0.999
Right bundle-branch block | 56 (9.2) | 85 (11.4) | 0.211 | 50 (10.6) | 60 (12.7) | 0.361
LVEF <35% | 17 (2.8) | 42 (5.6) | 0.011 | 17 (3.6) | 13 (2.8) | 0.579
Mean gradient, mmHg | 42.0 [31.3 – 50.0] | 44.0 [37.0 – 54.0] | <0.001 | 43.0 [34.0 – 52.0] | 42.5 [34.8 – 51.0] | 0.940
Bicuspid aortic valve | 20 (3.3) | 97 (13.0) | <0.001 | 20 (4.2) | 25 (5.3) | 0.542
Severe aortic valve calcification | 126/606 (20.8) | 206/747 (27.6) | 0.004 | 114 (24.3) | 115 (24.4) | 0.954
Asymmetric calcification | 123 (20.2) | 336 (44.9) | <0.001 | 120 (25.4) | 135 (28.6) | 0.305
Mean annulus diameter, mm | 23.7 [22.4, 25.1] | 24.9 [23.4, 26.2] | <0.001 | 23.8 [22.4, 25.2] | 24.9 [23.4, 26.2] | <0.001
CAUTION: In Europe, ACURATE neo and neo2 Aortic Valve Systems are CE-marked. In the USA, ACURATE neo2 is an investigational device and restricted under federal law to investigational use only. Not available for sale.
Pellegrini C. ACURATE neo2 versus SAPIEN 3 Ultra. EuroIntervention 2022.
Notes: Delivery Notes:
After 1:1 matching, the only significant difference seen in baseline characteristics is mean annulus diameter.

## Slide 11
Essential Outcomes
ACURATE neo2 & SAPIEN 3 Ultra
CAUTION: In Europe, ACURATE neo and neo2 Aortic Valve Systems are CE-marked. In the USA, ACURATE neo2 is an investigational device and restricted under federal law to investigational use only. Not available for sale.
 | ACURATE neo2 n=608 | SAPIEN 3 Ultra n=748 | p-value | ACURATE neo2 n=472 | SAPIEN 3 Ultra n=472 | p-value
Pre-dilatation, n (%) | 534 (87.8) | 268 (35.8) | <0.001 | 434 (91.9) | 148 (31.4) | <0.001
Post-dilatation, n (%) | 250 (41.4) | 111 (14.8) | <0.001 | 211 (44.7) | 69 (14.6) | <0.001
Procedural time, min | 44.0 [35.0 – 59.0] | 46.0 [35.0 – 58.0] | 0.867 | 45.0 [36.0 – 59.0] | 46.0 [35.0 – 57.0] | 0.472
Fluoroscopy time, min | 9.4 [7.0 - 13.3] | 10.2 [7.1 - 14.6] | 0.033 | 9.8 [7.3 - 13.8] | 10.2 [6.9 - 14.1] | 0.974
Technical success (VARC-3) | 575 (94.6) | 714 (95.5) | 0.529 | 448 (94.9) | 450 (95.3) | 0.880
Device success (VARC-3) | 557 (91.6) | 626 (83.7) | <0.001 | 434 (91.9) | 401 (85.0) | 0.001
Contrast agent, ml | 40.0 [20.0, 116.0] | 115.0 [36.0, 160.0] | <0.001 | 40.0 [22.0, 130.0] | 117.5 [37.8, 160.0] | <0.001
Pre-discharge moderate/severe PVL n (%)* | 4 (0.7) | 6 (0.8) | 1.000 | 3 (0.6) | 5 (1.1) | 0.723
Pre-discharge Mean gradient ≥ 20mmHg, n (%) | 11 (1.8) | 69 (9.3) | <0.001 | 11 (2.4) | 36 (7.7) | <0.001
Indexed effective orifine area (cm2)** | 0.9 [0.8, 1.1] (n=453) | 0.8 [0.7, 0.9] (n=261) | <0.001 | 0.9 [0.8, 1.1] (n=342) | 0.8 [0.7, 0.9] (n=167) | <0.001
Severe PPM, n (%)** | 10/453 (2.2) | 39/261 (14.9) | <0.001 | 10/342 (2.9) | 25/167 (15.0) | <0.001
Major vascular complication (VARC-3) | 39 (6.4) | 66 (8.8) | 0.122 | 29 (6.1) | 45 (9.5) | 0.069
Coronary obstruction requiring PCI | 1 (0.2) | 3 (0.4) | 0.768 | 1 (0.2) | 2 (0.4) | 0.999
Annular rupture, n (%) | 1 (0.2) | 2 (0.3) | 1.000 | 1(0.2) | 0 (0) | 0.999
Acute kidney injury St 2-4, n (%) | 18 (3.0) | 23 (3.1) | 0.999 | 15 (3.2) | 15 (3.2) | 0.999
30-day All-stroke** | 18/598 (3.0) | 23/734 (3.1) | 0.999 | 16/464 (3.4) | 11/465 (2.4) | 0.435
30-day Pacemaker implantation, n (%)** | 40/522 (7.7) | 70/664 (10.5) | 0.090 | 33/406 (8.1) | 43/419 (10.3) | 0.289
30-day mortality, n (%)** | 11/598 (1.8) | 18/734 (2.5) | 0.566 | 8/464 (1.7) | 11/465 (2.4) | 0.646
* Pre-discharge echocardiogram assessed. 10/1356 assessed by angio ** Data not available for full population. Sample sizes as indicated.
Pellegrini C. ACURATE neo2 versus SAPIEN 3 Ultra. EuroIntervention 2022.
Notes: Delivery Notes:
This is the 1st direct head-to-head comparative study of the 2nd generation ACURATE neo2 and 4th generation SAPIEN 3 Ultra valves, demonstrating favorable ACURATE neo2 outcomes:
  Paravalvular Leak: The rate of echocardiogram assessed moderate to severe PVL was low and similar for both THVs (0.6% vs. 1.1%, p=0.723). ACURATE neo2 recorded 32.8% mild and 66.5% none PVL rates1.
  Gradients: ACURATE neo2 demonstrated significantly lower mean gradients (9±4 vs 13±4 mmHg; p<0.001), and a lower rate of elevated (≥20mmHg) gradients (2.4% vs 7.7%; p<0.001) and significantly larger Indexed Effective Orifice Area (iEOAs) (0.92cm2 [0.79, 1.05] vs. 0.78 cm2 [0.67, 0.91]; p<0.001)‡. This translated into a significantly lower rate of severe prosthesis-patient mismatch (2.9% vs 15.0%; p<0.001‡) and a superior device success rate (91.9% vs. 85%; p=0.001) for ACURATE neo21
  Permanent Pacemaker Implantation: The 30-day new permanent pacemaker implantation rate was low and similar for both THVs (8.1% vs 10.3%; p=0.289)*1.
  In-Hospital & 30-day Events: Rates of in-hospital and 30-day events were overall low, and comparable between both THVs1.